## Slide 1
Design and Simulation of an Automatic Street Light Control System Using Combinational Logic
Presented by
M Sai Vidyanandh 260030579
V Sai Spoorthi 2620030569
V pranathi 2620030670
G Bharath 2620030574
G manideep 2620090053

## Slide 2
Abstract
Concept
Automatic street light control using combinational logic gates to reduce energy waste
Inputs
Ambient light intensity (LDR) and motion detection drive the control signal
Tool
Designed and simulated in Logisim using AND, OR, and NOT logic gates
Impact
40–50% energy savings compared to manual control systems

## Slide 3
Hardware and Software Requirements
Simulation Tools
Logisim — digital circuit design and simulation
Hardware Components
Logic gates: AND, OR, NOT, NAND
LDR sensor and motion sensor
LED indicator and relay module
Breadboard, jumper wires, resistors, capacitors
Power Supply
5V DC for logic circuits
12V DC for street light load

## Slide 4
CHAPTER 1
Design and Implementation
Exploring the system architecture, truth table, and Logisim circuit design.

## Slide 5
System Overview and Inputs
Light Sensor
Detects ambient light intensity
Outputs 1 when dark
Outputs 0 when bright
Motion Sensor
Detects vehicle or pedestrian movement
Outputs 1 when motion detected
Outputs 0 when idle
Output Signal
Street light control signal
1 = Light ON
0 = Light OFF

## Slide 7
Truth Table and Boolean Logic
Light sencor | Motion | Output (Light)
0 | 0 | 0 — OFF
0 | 1 | 0 — OFF
1 | 0 | 0 — OFF
1 | 1 | 1 — ON
Key Conditions
Light turns ON only when dark AND motion is detected
Light stays OFF when bright, regardless of motion
Light stays OFF at night when no motion is present
Boolean Expression: Output = LDR AND Motion

## Slide 8
Circuit Design in Logisim
Street Light
Relay Module
AND Gate
LDR Input
Implementation Steps
1
Motion Input
Motion sensor connected to AND gate (positive logic)
2
AND Gate Output
Drives the relay module to control the street light
3
LED Indicator
Visual status indicator for light state in simulation

## Slide 9
Working Principle
Day Mode
LDR = 0 (bright)
AND output = 0
Light stays OFF
Night — No Motion
LDR = 1, Motion = 0
AND output = 0
Light stays OFF
Night — Motion Detected
LDR = 1, Motion = 1
AND output = 1
Light turns ON ✅

## Slide 10
CHAPTER 2
Results and Testing
Verifying all test cases, measuring performance, and confirming energy efficiency outcomes.

## Slide 11
Simulation Results
4
Test Cases
All verified in Logisim simulation
<1ms
Response Time
Combinational logic, zero propagation delay
50%
Energy Saved
Compared to always-on manual systems
Power Consumption Breakdown
Component | Power
Logic Circuit | 50 mW
LED Street Light Load | 60 W